## Slide 1: Key Questions
How can a continuous wave form be converted into discrete samples?
How can discrete samples be converted back into a continuous form?

## Slide 2: Characteristics of Sound
Amplitude
Wavelength (w)
Frequency ( )
Timbre
Hearing: [20Hz – 20KHz]
Speech: [200Hz – 8KHz]

## Slide 3: Digital Representation of Audio
Must convert wave form to digital
  sample
  quantize
  compress

## Slide 4: Sampling (in time)
Measure amplitude at regular intervals
How many times should we sample?

## Slide 5: Example
Suppose we have a sound wave with a frequency of 1 cycle per second

## Slide 6: Example
If we sample at one cycle per second, where would the sample points fall?

## Slide 7: Example
If we sample at 1.5 cycles per second, where will the sample points fall?

## Slide 8: Sampling - Example
If we sample at two cycles per second, where do the sample points fall?

## Slide 9: Nyquist Theorem
For lossless digitization, the sampling rate should be at least twice the maximum frequency response.
In mathematical terms:
fs > 2*fm
where fs is sampling frequency and fm is the maximum frequency in the signal

## Slide 10: Nyquist Limit
max data rate = 2 H log2V bits/second, where H = bandwidth (in Hz) V = discrete levels (bits per signal change)
Shows the maximum number of bits that can be sent per second on a noiseless channel with a bandwidth of H, if V bits are sent per signal
  Example: what is the maximum data rate for a 3kHz channel that transmits data using 2 levels (binary) ?
  (2x3,000xln2=6,000bits/second)

## Slide 11: Limited Sampling
But what if one cannot sample fast enough?

## Slide 12: Limited Sampling
Reduce signal frequency to half of maximum sampling frequency
  low-pass filter removes higher-frequencies
  e.g., if max sampling frequency is 22kHz, must low-pass filter a signal down to 11kHz

## Slide 13: Sampling Ranges
Auditory range 20Hz to 22.05 kHz
  must sample up to to 44.1kHz
  common examples are 8.000 kHz, 11.025 kHz, 16.000 kHz, 22.05 kHz, and 44.1 KHz
Speech frequency [200 Hz, 8 kHz]
  sample up to 16 kHz
  but typically 4 kHz to 11 kHz is used

## Slide 15: Quantization

## Slide 16: Quantization
Typically use
  8 bits = 256 levels
  16 bits = 65,536 levels
How should the levels be distributed?
  Linearly? (PCM)
  Perceptually? (u-Law)
  Differential? (DPCM)
  Adaptively? (ADPCM)

## Slide 17: Pulse Code Modulation
Pulse modulation
  Use discrete time samples of analog signals
  Transmission is composed of analog information sent at different times
  Variation of pulse amplitude or pulse timing allowed to vary continuously over all values
PCM
  Analog signal is quantized into a number of discrete levels

## Slide 18: PCM Quantization and Digitization
Digitization
Quantization

## Slide 19: Linear Quantization (PCM)
Divide amplitude spectrum into N units (for log2N bit quantization)
Sound Intensity
Quantization Index

## Slide 20: Non-uniform Quantization

## Slide 21: Perceptual Quantization (u-Law)
Want intensity values logarithmically mapped over N quantization units
Sound Intensity
Quantization Index

## Slide 22: Differential Pulse Code Modulation (DPCM)
What if we look at sample differences, not the samples themselves?
  dt = xt-xt-1
  Differences tend to be smaller
    Use 4 bits instead of 12, maybe?

## Slide 23: Differential Quantization (DPCM)
Changes between adjacent samples small
Send value, then relative changes
  value uses full bits, changes use fewer bits
  E.g., 220, 218, 221, 219, 220, 221, 222, 218,.. (all values between 218 and 222)
  Difference sequence sent: 220, +2, -3, 2, -1, -1, 3, ..
  Result: originally for encoding sequence 0..255 numbers need 8 bits;
  Difference coding: need only 3 bits

## Slide 24: Adaptive Differential Pulse Code Modulation (ADPCM)
Adaptive similar to DPCM, but adjusts the width of the quantization steps
Encode difference in 4 bits, but vary the mapping of bits to difference dynamically
  If rapid change, use large differences
  If slow change, use small differences

## Slide 25: Signal-to-Noise Ratio

## Slide 26: Signal To Noise Ratio
Measures strength of signal to noise
  SNR (in DB)=
Given sound form with amplitude in [-A, A]
Signal energy =
A
0
-A

## Slide 27: Quantization Error
Difference between actual and sampled value
  amplitude between [-A, A]
  quantization levels = N
e.g., if A = 1, N = 8, = 1/4

## Slide 28: Data Rates
Data rate = sample rate * quantization * channel
Compare rates for CD vs. mono audio
  8000 samples/second * 8 bits/sample * 1 channel = 8 kBytes / second
  44,100 samples/second * 16 bits/sample * 2 channel = 176 kBytes / second ~= 10MB / minute

## Slide 29: Comparison and Sampling/Coding Techniques

## Slide 30: Summary