## Slide 1: ICS 2207 Multimedia Applications
Lecture 2d: Multimedia Data Processing(Sound, Image/Video)

## Slide 2: Areas of Application of Digital Technology
Computers
New telephone networks and capabilities e.g video conferencing etc
Digital television technology -e.g Interactive TV, Video o

## Slide 3: Digital Technology Concepts
Digitization of information is an important step in processing data
Basics
  Digital signals that could be assigned digital values
Digital computer technology
  Digital signals
  Binary representation
    Encoded into ones and zeros

## Slide 4: Advantages Digital Signals
Native language of the computer-Information can be processed by the computer
Control programmable services
Better quality due to being able to reconstruct exact digital patterns at the receiving end
Faster communication speeds are possible
Easy transmission of information over the Internet and other computer networks
Minimize loss of quality during transmission

## Slide 5: Digital Signal
1 0 1 1 0 1 0 0
Pulse
Time
Signal Strength
Pulse Duration

## Slide 6: Digitization of Information
Information need to be digitized for computer processing and the transmission of information
Convert into digital form for processing storage and transmission

## Slide 7: Components of Information
Alphanumeric data
Image
Audio
Video

## Slide 8: Digital Information Processing
Data
Audio
Image
Video
Digitized and Encoded
Digital
Transmission

## Slide 9: Digitization Of Alphanumeric Data
Alphanumeric data is digitized using well established coding systems
  Unicode
  EBCDIC
  ASCII
  Etc
  See notes on encoding schemes

## Slide 10: Digitization Of Audio

## Slide 11: Digitization Of Audio: Overview
Take samples of audio at pre-determined time intervals known as the sampling rate
Represent the sampled audio with digital signals
  Pulse Amplitude Modulation (PAM)
Encode signals into binary code
  Pulse Code Modulation (PCM) that incorporates PAM as well
  Required for computer processing

## Slide 12: Digitization of Audio: Pulse Amplitude Modulation (PAM)
Audio
9 8 7 6 7 9
Digital Signals must further be encoded into binary signals for computer processing and transmission.
Sampling Interval

## Slide 13: Digitization and Encoding of Audio: Pulse Code Modulation (PCM)
PCM is a two step process
First the audio is sampled and represented by digital signals
The digital signals are then encoded in binary form
Assign 1 Q1. Define signal sampling and show how it is used to in processing audio data

## Slide 14: Binary Encoding of Signals in Pulse Code Modulation (PCM)
9 8 7 6 5 6
1001 1000 0111 0110 0101 0110
The integer numbers have effectively been coded into zeros and ones. The ones and zeros now contain the audio information encoded in a form that could be processed by a computer.
PCM

## Slide 15: Salient Points on the Digitization Of Audio
Sampling rate? and the number of bits? used for representing the samples will determine the quality of the audio
Quality is retained in transmission because only codes are transmitted
Audio can be recreated to the original quality by extracting the pattern from the digital code

## Slide 16: Sampling Factors
Sampling interval determined by sampling frequency
  Measured in Hz
Sampling depth
  Measured in number of bits used to encode the sample
Sampling channels
  Mono or stereo, for example 1 for mono and 2 for stereo
  Assign: Distinguish between the two and illustrate it use and advantages

## Slide 17: Sampling Example
CD quality audio
  44 KHz
  16 Bits
  Stereo

## Slide 18
Audio Quality, Bandwidth and Streaming

## Slide 19: Factors Affecting Quality
Number of bits used for binary encoding. Example: 4 bits allow 16 amplitude variations to be represented. 24=16
9 8 7 6 7 9
Sampling Interval

## Slide 20: Effect of Sampling Frequency
Higher sampling frequency
  Smaller sampling intervals, time between samples
  Frequent sampling
  Better quality because the audio pattern is captured better
  Higher bandwidth required for transmission
  Higher disk space required for storage

## Slide 21: Computation of Bandwidth Requirement for Transmission
Problem:
  Compute the audio streaming rate for a voice grade circuit given that the number of bits used in the sampling is 8
Background information
  A voice grade circuit has a bandwidth of approximately 4000 Hz
General rule
  For acceptable quality, the audio must be sampled at twice the frequency of the voice grade bandwidth

## Slide 22: Reason for Sampling at Twice the Frequency
According to Nynguist Theorem
Two peaks in each cycle
  Half of a cycle is above the datum line
  The other half of the cycle is below the datum line
Therefore, sample the audio at twice the frequency rate

## Slide 23: Example CD Sampling
Sampling in this case is done for higher quality
  44 KHz
  16-bits
  Stereo

## Slide 24: Problem Representation
79 68 57 46 57 79
1/8000 Seconds (8000 HZ twice the frequency of the voice
grade circuit)
or 2X4000 samples per second
8 bits are used enabling
256 amplitudes to
represent the human
voice which is considered
to be adequate.

## Slide 25: Bandwidth Computation for Voice
Number of samples
  8000 per second
Number of bits per sample
  8
Bandwidth requirement
  8X8000 bps = 64,000 bps
  Approximately 64K bps
64K bps is the speed of a single ISDN (B) channel designed to carry voice

## Slide 26: Bandwidth of Voice Circuits
Generally speaking, the bandwidth requirement for uncompressed voice circuit is 64 Kbps
An example is the ISDN – B channel that was originally intended to carry voice
  Its bandwidth is 64 K bps

## Slide 27: Examples in Audio Quality and Bandwidth Requirement
CD quality
  44,100 Hz, 16 bit, Stereo
  1376K bps
Radio quality
  22,050 Hz, 8 bit, mono
  176K bps
Telephone quality
  11,025 Hz, 8bit, mono
  88K bps

## Slide 28: Audio Transmission In WWW
Client
Receive audio using
Internet Explorer
and a plug-in to receive
the audio stream.
Audio streaming requires compression.
Real-time audio
broadcast support
using streaming
server module.
28-56K bps
Web
Site

## Slide 29: Delivery of Instruction Over the WWW
Client
Web
Site
Receive audio/video using
Internet Explorer and Media
Player.
Audio/Video streaming.
Store streamed audio/
video using Windows Media.
28-56K bps

## Slide 30: Types of Multimedia Transmission
Unicasting
Multicasting
Broadcasting

## Slide 31: Sampling Considerations In Communications
Sender
Receiver
Digital audio transmission
Adjust quality (sampling interval and bit
representation) to suit bandwidth availability.

## Slide 32: Audio Files
Audio can be stored in different formats
  Uncompressed or raw file format (wav)
  Compressed format
  Streaming format
    Streamed audio is also compressed
    It is also designed for real-time delivery of audio

## Slide 33: Audio File Format
wav file format
  Basic file format in audio storage or raw file
rm file format
  Real audio’s streamed file format
  Streamed file
wma file format
  Microsoft’s audio streamed file format
  Streamed file
mp3 file format
  Compressed file
aac file format

## Slide 34
Quality Retention in Digital Transmission

## Slide 35: Quality Retention
Quality is retained in digital transmission because only the codes are transmitted
Quality is subject to some deterioration in analog transmission because the wave pattern is transmitted

## Slide 36: Analog Audio Transmission
Audio Prior
to Transmission
Audio with
Interference
Transmission
Audio After Filtering

## Slide 37: Passage of Analog Audio Over Analog Lines
Analog
Audio
Analog
Signals
Analog
Signals
Analog
Audio
Telephone
Telephone

## Slide 38: Recreation of Audio from Analog Signals
A difficult task
Complex algorithms are used to filter noise etc. for better audio transmission

## Slide 39: Signal Passage in Digital Audio Transmission
Encode
Transmit
Recreate
Decode
Audio
Audio

## Slide 40: A Sample Digital Audio Transmission Path
Analog
Audio
Digital
Audio
DSL
Modem
DSL
Modem
Digital
Audio
Analog
Audio
Sound
Card
Sound
Card
Digital
Network

## Slide 41: Sound Generation
Sound is recreated at destination
  Using FM synthesis
  Using wave table generation
Noise is not an issue in digital communication although it is an issue in digital transmission
  The reason, once again, is due to the fact that only codes are transmitted in digital transmission

## Slide 42: Better Sound Generation
Wave table generation provides better sound reproduction that FM synthesis

## Slide 43: Digital Advantage in Audio Transmission
Only codes are transmitted
Original encoding is recreated
Original audio is reproduced
Again, sampling rate and number of bits used in each sample will determine the quality of audio transmitted

## Slide 44: Digitized Signal Transmission Over Analog Lines
Encode
Transmit
Recreate
Decode
Audio
Audio
Sampled Signals

## Slide 45: Sample Digital Audio Transmission Path Over Analog Lines
Analog
Audio
Digital
Audio
Modem
Modem
Digital
Audio
Analog
Audio
Sound
Card
Sound
Card
Analog
PSN

## Slide 46: Audio Transmission In WWW
Client
Web
Site
Receive audio using
Internet Explorer
and Windows Media Player.
Audio stream over analog/digital line.
Real-time audio
broadcast support
using Windows Media
streaming server module.

## Slide 47: Analog to Digital Converter
A to D and D to A converter
The chip that is responsible for this conversion is known as the DSP (Digital Signal Processor) chip
It is used in sound cards, modems etc. wherever there is a need for A to D and D to A conversion
The mass use of this chip in various devices has led to a drastic drop in the price of the chip and the devices

## Slide 48: Digital Signal Processor (DSP)
DSP
Digital
Analog

## Slide 49
Digitization Of Image

## Slide 50
Image representation methods

## Slide 51: Bitmap Graphic
A image is divided into a matrix of pixels, where each pixel is a small dot.
  More pixels 
  Better representation of image 
  Better resolution 
  More memory
Each pixel is assigned a bit pattern. The size and the value of the pattern depend on the image.

## Slide 52
Figure 2-7
Bitmap graphic method of a
black-and-white image

## Slide 53
Figure 2-8
Representation of color pixels
Color image
  Each pixel is decomposed into 3 primary colors: red, green and blue. (RGB)
  The intensity of each color is measured, and a bit pattern (8 bits) is assigned.

## Slide 54: Resolution
The term is most often used to describe monitors, printers, and bit-mapped graphic images.
Dot-matrix and laser printers, the resolution indicates the number of dots per inch. For example, a 300-dpi (dots per inch) printer is one that is capable of printing 300 distinct dots in a line 1 inch long. This means it can print 90,000 dots per square inch.
Graphics monitors, the screen resolution signifies the number of dots (pixels) on the entire screen. For example, a 640-by-480 pixel screen is capable of displaying 640 distinct dots on each of 480 lines, or about 300,000 pixels.

## Slide 55: Vector Graphic
A image is decomposed into a combination of curves and lines.
Each curve or line is represented by a mathematical formula.

## Slide 56: Audio
Audio is a representation of sound or music.
Audio is by nature analog data.
It is continuous, not discrete.
Audio is converted to digital data and stored in bit patterns.
  Sampling
  Quantization
  Coding
  Stored

## Slide 57
Figure 2-9
Audio representation

## Slide 58: Video
Video is a representation of images (frames) in time.
A movie is a series of frames shown one after another to create the illusion of motion.
Today video is normally compressed.

## Slide 59: Image Digitization
Image can be of the form black and white, gray scales, color
Factors that influence the digitization of image are as follows
  Resolution measured in pixels
  Color depth expressed in number of color variations

## Slide 60: Digitization Of Image: Overview
Pixel
Horizontal Resolution
Vertical Resolution

## Slide 61: Digitization of the Letter L
Number of bits
determine the
amount of
information that could
be stored.

## Slide 62: Digitization Of Image: The Process
Divide the image into a grid of pixels that may be considered as the sampling points of the image
Digitize information on each pixel
Store and transmit

## Slide 63: Resolution
Horizontal resolution
  Number of horizontal pixels
Vertical resolution
  Number of vertical pixels
Image resolution
  Horizontal by vertical resolution
  Ex: 640 by 480

## Slide 64: Digitization of Black and White Image
White
  A pixel lit represents a 1
Black
  A pixel not lit represents a 0
Storage required per pixel
  1 bit
Storage required for 640 by 480 resolution image
  640 times 480 bits = 307,200 bits = 38.4K Bytes

## Slide 65: Digitization of Image Using Gray Scales
A pixel may take a value between 0 and 15 for 16 gray scales
A gray scale of 3 can be coded as 0011 and the others similarly using this 4 digit code
The bandwidth requirement for the transmission of a 640X480 image in this case is as follows:
  640X480X4 = 153.5K Bytes

## Slide 66: Digitization of Color Image
Image coding
  Each pixel may take a value between 0 and 255 if 256 colors are to be represented
Storage requirement
  Digitizing of images requires substantial number of bytes and hence large storage space for processing
Bandwidth requirement
  Higher bandwidths are required to transmit color images

## Slide 67: Bandwidth Computation for Image with 256 Colors
Resolution is 640X480
8 bits are required to represent 256 colors
bandwidth requirement for the transmission of one image is as follows:
  640X480X8 = 307.2K Bytes

## Slide 68: The Effect of Color Depth and Resolution
Compare VGA, SVGA and XGA
  XGA provides the highest resolution
Practical implication
  More colors less resolution if bandwidth or storage is the limiting concern
  Example
    256 colors at lower resolution
    16 colors at higher resolution
Rule
  Higher the resolution the lower the number of colors available in general given the resource constraints such as bandwidth constraints

## Slide 69: Factors Affecting Bandwidth Requirement in Image Transmission
The higher the resolution, the higher the bandwidth requirement for transmission
The higher the color representation, also known as color depth, higher the bandwidth requirement
For true color, 24 (32) bits are required to represent each pixel
The file sizes in raw image capture can thus become very large

## Slide 70
Compression of Digitized Images

## Slide 71: Compression of Digitized Images
Compression is required to reduce the size of the image file
Large blocks of unchanged data in an image (background) offers an opportunity to compress the image
Image files are almost always compressed

## Slide 72: A Few Compression Formats
GIF
JPEG
MIC (Microsoft Image Composer)
PCD (KODAK) - Used by Corel
Uncompressed file exist in the form of bit mapped file with the extension of .BMP

## Slide 73: Image File Format Extensions
File formats often represent the compression procedure being used such as jpg representing the jpeg compression technique
Examples:
  Bmp – uncompressed file format
  Gif
  jpg
  pcd
  tiff
  pcx

## Slide 74: Loss-less Compression and Others
Some compression formats offer loss-free compression of the image
Others sacrifice minimal loss for the sake of reduced storage and bandwidth requirements
Fortunately, the loss is not easily detected by the naked eye

## Slide 75: Image Transmission Considerations
Sender
Receiver
Adjust image to suit available bandwidth.
Adjustable features are as follows.
- Resolution
- Color depth
Adjusting the size also reduces the bandwidth
requirement because of a corresponding reduction
in the number of pixels required to represent
the image.

## Slide 76: A Peek At Data Compression
0 0 0 0 0 0 0 0 0 0 0 - - - - - -0 1 1 1 1 1 11 …... 0
THE ABOVE CAN BE COMPRESSED INTO = #9000$0#
  9000 bits are compressed into 8 characters that require approximately 64 bits for transmission
  9000 ZEROS ARE CODED INTO #900$0#
#600$1#
INTERPRET WITHIN THE # SIGN
600
NUMBER COUNT
1
CHARACTER BEING
TRANSMITTED

## Slide 77: Compression Result
In the previous example, 9000 bits are compressed into 8 characters
If 10 bits are used on the average for transmitting each character, the 9000 bits of information is now compressed into 80 bits for transmission

## Slide 78: Modem Implication in Image Transmission
Modems also compress the data stream to achieve higher transmission speeds
Because of the fact that the images are already compressed, the full speed benefit may not be realized when images are transmitted over a modem connection
An already compressed image file does not, for instance, offer itself well to further compression in the modem

## Slide 79: Module
Digitization Of Video

## Slide 80: Digitization of Video
Digitization of video is an extension of the process of digitizing an image
It amounts to the transmission of certain number of still images known as frames per second
Obviously, digitized video requires higher bandwidth for transmission and more space for storage

## Slide 81: Frame Rate
30 frames of images per second, in general, defines continuos motion
In communications, 25 frames per second is considered to be continuous motion
15 frames per second is currently used in video conferencing over digital lines for acceptable reception of video
It is also possible to engage in video conferencing at a frame rate of 5 frames per second

## Slide 82: Computation of Bandwidth for Raw Transmission of Video
Image resolution is 640X480
Number of colors is 256 (8 bit)
Acceptable reception requires 15 frames per second
Therefore, the bandwidth for the raw transmission is as follows:
  640X480X8X15 = 36.86M bps = 4.6M Bps

## Slide 83: Compression Standards Used in the Digitization of Video
MPEG 1, MPEG 2, MPEG 3 and MPEG 4
Windows Media Video
Real Media
Indio
QuickTime
ActiveMovie
AVI

## Slide 84: Streaming Formats for Video
Various streaming formats are supported by different vendors
  RealVideo
Microsoft’s streaming format
  wma (Windows Media Audio)
  wmv (Windows Media Video)
  Active Streaming Format (ASF)
Apple’s QuickTime format
Etc.

## Slide 85: Overview of Video Transmission in Video Conferencing
Minimum speed
  3 to 5 frames per second
Acceptable speed
  15 frames per second
Transmission techniques
  Data is compressed
  Only changes to the frame are transmitted

## Slide 86: Bandwidth Optimization in Video Conferencing
Minimize Windows for maximum efficiency
  Transmit less number of pixels in minimized form
Decrease the resolution
  Has the same effect as above
Decrease the number of colors displayed

## Slide 87: Communication Links for Video Conferencing
Possible on analog lines using 56,000 bps transmission speed but not desirable
Digital lines are preferred and the guidelines are as follows:
  Possible at 128k bps using ISDN lines
  Acceptable at 384k bps
  1M bps and above offer good quality video transmission

## Slide 88: ISDN Line Suitability
ISDN B channels can be assigned on a dynamic basis depending on the bandwidth requirement at any point in time during video conferencing

## Slide 89: Video Conferencing Products
Intel ProShare
CU-See Me
Picturetel
C-phone
etc.

## Slide 90: End of Lecture