## Slide 1: ICS 2306 Computer Networks Course Syllabus
Topology and architecture of Computer Networks
Layered Protocols: OSI and TCP/IP
Local area networks
Wide area networks
Routing protocols
Gatewaying

## Slide 2: Architecture of Computer Networks
Networking Cabling- the physical media
There are three major groups of cabling that exist for networks. These are:
Coaxial
Twisted pair: Unshielded Twisted pair, Shielded Twisted Pair
Fiber- optic.

## Slide 3: Networking Cabling- the physical media
Cables differ by their properties. Some of the characteristics you will consider may include:
Cost
Installation and skills required
Capacity of the cables chosen (cable speed/bandwidth) in bits per second.
Attenuation (maximum distance). The fading of the electrical signal over a distance.

## Slide 4: Networking Cabling- the physical media
Immunity to interference: This concerns how well the cable holds up against interference e.g. electromagnetic interference (EMI). Supposing you needed to run a network into a manufacturing facility with a lot of heavy machinery that use electrical motors, an unshielded type of cable may not be the best choice in that situation.

## Slide 5: Co-Axial Cable.
A center conductor wire surrounded by layer of insulation and metallic sheath
Commonly used to connect to cable TV
Higher bandwidth and less susceptibility to noise than twisted pair

## Slide 6: Co-Axial Cable.
The co-axial cable has two conductors parallel to each other or on the same axis. The centre conductor is copper, outside the copper is a non-conductive material used separate the inner conductor from the outer. The outer conductor is a fine mesh made from copper. It is used to help shield the cable from EMI. Outside the copper mesh is the final protective cover.

## Slide 7: Co-Axial Cable.
The actual network data travels through the centre conductor in the cable. EMI is caught by the outer copper mesh. It should be grounded to dissipate the electrical interference. The importance of stranded wire is the ability to bend the cable. There are many types of co-axial cables, it all depends on the type of network you plan to use.

## Slide 8: Co-Axial Cable.
The cables vary by gauge and impedance. W. The higher the RG number the thinner the central conductor core -here gauge is the measure of the cables thickness measured in Radio Grades(RG) number, 18 gauge wire is thicker than 24 gauge wire. Usually the gauge number is printed on the side of the cable. The measure of resistance in the cable is called impedance. Each different type of network uses a different resistance.

## Slide 9: Co-Axial Cable.
Each piece of equipment attaching to the cable must use same impedance. This means all Network Interface Cards (NICs), terminators and cable segments must be the same. The conducting core and the wire mesh must always be separated, if they touch the cable will experience a short and noise or stray signals on the mesh will flow onto the copper wire. This will destroy the data signal.

## Slide 10: Types of Co-axial cable.
Thinnet: this is a flexible coaxial cable about 0.25 inches thick and easy to work with. Networks that use thinnet have the cable connected directly to a computer network adapter card. It can carry a signal upto 185 metres before the signal starts to suffer from attenuation. It is in a group called the RG-58 family and has a 50-ohms impedance. The difference in the RG-58 is the centre core of copper, it can either be a stranded wire or a solid copper core. RG-58/U is solid copper core, RG-58 A/U is a stranded wire core.

## Slide 11: Types of Co-axial cable.
Thicknet: it’s a relatively rigid coaxial cable about 0.5 inch in diameter. Sometimes referred to as standard Ethernet. The copper core is thicker than a thinnet core. The thicker the copper core the further the cable can carry signals. Thicknet can carry signals up to 500 metres. It is sometimes used as a backbone to connect several smaller thinnet based networks.

## Slide 12: Types of Co-axial cable.
A device called a transceiver connects the thinnet coaxial to the larger thicknet coaxial cable. A transceiver includes a connector called a vampire tap to make the actual physical connection to a thicknet core. Connection from the transceiver to the network adapter card is made using a transceiver cable (drop cable) to connect to the Attachment Unit Interface (AUI) port connector on the card. An AUI port is also known as DB-15 connector or Digital Intel Xerox (DIX). Thicknet is more expensive and difficult to work with since cant bend easily but will carry a signal farther.

## Slide 13: Coaxial Connection Hardware
Both thinnet and thicknet use connection components known as BNC (British Naval Connector) to make connections between the cable and the computers.
The BNC cable connector : the BNC cable connector is crimped to the end of the cable
The BNC T connector: this connector joins the network interface card in the computer to the network cable.
BNC barrel connector: this connector is used to join two lengths of thinnet cable to make one longer one.
BNC Terminator: It closes each end of the bus cable to absorb stray signals.

## Slide 14: TWISTED PAIR CABLE
It consists of two insulated strands of copper wire twisted around each other. There are two types:
Unshielded twisted pair
Shielded twisted pair

## Slide 15: TWISTED PAIR CABLE
It is light weight, easy to install, inexpensive and supports many different types of networks. supports speeds of up to 100mbps. The copper core of the cable is usually 22 AWG or 24 AWG ( American wire Gauge). A number of twisted pair wires are grouped together and enclosed in a protective sheath to form a cable. The twist is to cancel out electrical noise from adjacent pairs.

## Slide 16: Unshielded Twisted Pair
Unshielded twisted pair is the most common. It can either be of voice grade or data grade depending on its application. It has an impedance of 100 ohms. There are five levels of data grade cabling :
Category 1: this category is intended for use in telephone lines and low speed data cable
Category 2: includes cabling for lower speed networks. this can support up to 4Mbps. Consists of four twisted pairs.

## Slide 17: Unshielded Twisted Pair
Category 3: This is a popular category for standard Ethernet networks. Supports up to 16Mbps but most often used in 10 Mbps. Consist of four twisted pairs.
Category 4: used for longer distances and higher speeds than category 3.
Category 5: Can support up to 1000Mbps. Has four twisted pair of copper wire.

## Slide 18: Shielded Twisted Pair
STP uses a woven braid jacket which is of higher quality more protected than UTP. It also uses a foil wrap between and around the wire pairs. This gives STP an excellent shielding to protect the transmitted data from outside interference. This then allows for higher transmission rates and longer distance without error.

## Slide 19: Shielded Twisted Pair
There are five levels of data grade cabling :
Type 1: Features two pairs of 22 AWG with each pair foil wrapped inside another sheath that has a wire braid ground.
Type 2 : This includes type 1 with four telephone pairs. Sheathed to the outside to allow one cable to an office for both voice and data.
Type 6: this features two pairs of stranded shielded 26 AWG to be used for patch cables.
Type 7: consists of one pair of stranded 26 AWG
Type 9: Two pairs of shielded 26 AWG

## Slide 20: Twisted Pair Cabling Components
Connection Hardware: twisted pair uses RJ45 connector to connect to a computer. The telephone connection uses RJ 11. RJ45 houses eight cable connections and RJ 11 houses four.
Distribution racks and rack shelves: Distribution racks and rack shelves can create room for more cables. It provides a good way to centralize and organize a network with many connections.
Expandable Patch panel : Supports up to 96 ports
Jack Couplers: These single or double RJ-45 jacks snap into patch panels and wall plates.

## Slide 21: FIBRE OPTIC
Use light instead of electricity to send data
Much higher bandwidth than coaxial cable
Immune to electrical interference
Materials cheaper than coaxial, but installation costs high

## Slide 22: FIBRE OPTIC
Optical fibre consists of thin cylinder of glass called the core, surrounded by a concentric layer of glass known as cladding. Sometimes plastic is used but cannot carry light pulses as far as glass. Each glass strand passes signals in only one direction so a cable consists of two strands in separate jackets. One strand transmits and the other receives.

## Slide 23: FIBRE OPTIC
Fiber optic cable transmissions are not subject to electrical interference and are extremely fast. Can transmit up to 1Gbps and over long distances. Optical fibre carry digital data signals in the form of modulated pulses of light.

## Slide 24: WIRELESS MEDIA
These do not use any physical connections between the two devices communicating. The three main types of wireless media are:
Radio wave
Micro Wave
Infrared

## Slide 25: Radio Waves
Radio waves frequencies between 10GHZ and 1GHZ. They include the following types
Short wave
Very high frequency (VHF) television and radio
Ultra High Frequency (UHF) TV and radio.

## Slide 26: Radio Waves
Most radio frequencies are regulated. However there are some frequencies that are not regulated they include:
902-928
2.4 GHZ internationally unregulated
5.72-5.85 GHZ

## Slide 27: Radio Waves
There are limits set on the amount of power that devices can broadcast in these frequencies. Radio waves can be broadcast in one direction. There are several antennas to choose from e.g. radio tower, half wave dipole, random length wire and yagi.

## Slide 28: Radio Waves
Radio wave transmission can be divided into three categories which are:
Low-power single frequency: the normal operating range in this type is 20-25 metres. It is the cheapest wireless media type. The speed vary from 1Mbps to 10 Mbps which is perfect for a small LAN. Attenuation is a problem due to the low power output allowed. EMI could be a problem because other devices could operate on the same frequency. Perfect for an office where everyone has a portable computer.

## Slide 29: Radio Waves
High power single frequency: can communicate over longer distances. It is more costly. Supports 1Mbps to 10 Mbps

## Slide 30: Radio Waves
Spread Spectrum: Uses several frequencies at once to provide reliable data transmissions that are resistant to interference. Direct sequence modulation and frequency hopping are two methods used in spread spectrum. Direct sequence breaks data into chips and transmits the chips across several frequencies. The receiver knows which data to collect on the different frequencies and assembles the data accordingly. It provides 2-6 Mbps transmission rates. Frequency hopping uses strict timing to switch frequencies at a specific time. Bursts of data are sent on one frequency and then the machines switch to another frequency for the next data burst. It has a transmission rate of 2Mbps.

## Slide 31: MICROWAVES
They travel at higher frequencies than radio waves and provide better throughput as a wireless network media. Microwave transmissions require the sender to be within sight of the receiver. They use licenced frequencies. They can be utilised on the following two types of communication system.

## Slide 32: MICROWAVES
Terrestial: They are used to transmit wireless signals across a few miles. These are used to cross roads or other barriers that make cable connection difficult. It requires that antennas be pointed at each other . Relay towers can be used as repeaters to extend the distance of the transmission.

## Slide 33: MICROWAVES
Satellite: Satellite microwave transmission are used to transmit signals throughout the world. These systems use satellites in orbit about 50,000 km above the earth. Satellite dishes are used to send the signal to the satellite where it is sent back down to the receivers satellite. They use directional antennas within the line of site. It is expensive and complicated, it involves launching a satellite into orbit.

## Slide 34: Satellite Transmission
Description
A form of microwave transmission
  Satellite acts as relay station
Components
  Earth station sends and receives signal to satellite
  Transponder receives and amplifies signal, changes frequency, and retransmits data
Useful when signal must travel thousands of miles
Diagrammatic representation

## Slide 35: INFRARED
Infrared frequencies are high and allow high speed data transmission. This technology is similar to the use of a remote control for TV. This transmission can be affected by objects obstructing the sender or receiver and by light sources. These are immune to EMI. There are two categories

## Slide 36: INFRARED
Point-Point: These type utilizes focused beams to transfer signals directly between two systems. It requires direct alignment between devices. It does not require license and it is immune to EMI. Anything that blocks the path of the beam is easily noticeable.

## Slide 37: INFRARED
Broadcast: They use a spread signal, broadcast in all directions instead of a direct beam. This helps to reduce the problems of proper alignment and obstruction. The disadvantage is reduced transmission rate.

## Slide 38: Networking Devices
Some network devices play a small role such as amplifying data to lengthen transmission distances, others have a larger role such as intelligently directing data traffic to avoid congestion. These devices include communication servers, multiplexers, repeaters, bridges, routers and hubs.

## Slide 39: Routers
Routing is the act of moving information across a network from a source to a destination. It occurs at the network layer and involves two basic activities.
Determining optimal routing path
Transporting packets through a network ( packet switching)

## Slide 40: Routers

## Slide 41: Routers
Path Determination: Routing protocols use metrics to evaluate what path will be the best for a packet to travel. A metric is a standard of measurement e.g path bandwidth, which is used by routing algorithms to determine the optimal path to a destination. To aid the process of path determination, routing algorithms initialize and maintain routing tables which contain route information. Route information varies depending on the routing algorithm used.

## Slide 42: Routers
Routing tables can also contain other information e.g. data about the desirability of a path. Routers compare metrics to determine optimal routes and these metrics differ depending on the design of the routing algorithm used. Routers communicate with one another and maintain the routing tables through the transmission of a variety of messages.

## Slide 43: Routers
The routing update message is one such message that consists of all or part of a routing table. By analysing routing updates from all other routers, a router can build a detailed picture of a network topology.
A link-state advertisement-message sent between routers informs other routers of the state of the senders link. Link information can be used to build a complete picture of network topology to enable routers to determine optimal routes to network destinations.

## Slide 44: Routers
Packet Switching: Switching algorithms are same for most routing algorithms. A host determines that it must send a packet to another host. Having acquired a routers address, the source host sends a packet addressed specifically to a routers physical (MAC) address, this time with the protocol (network layer) address of the destination host. As it examines the packets destination protocol address, the router determines that it either knows or does not know how to forward the packet to the next hop.

## Slide 45: Routers
If the router does not know how to forward the packet, it drops the packet. If it knows, it changes the destination physical address to that of the next hop and transmits the packet. If the next hop is not the ultimate destination host, the hop is usually another router which executes the same switching decision process. As the packet moves through the network, its physical address changes but the protocol address remains constant.

## Slide 46: Routing Algorithms
Routing algorithms can be differentiated based on several key characteristics namely:
The particular goals of the algorithm designer affect the operation of the resulting routing protocol
Various types of routing algorithms exist and each algorithm has a different impact on the network and router resources.
Routing algorithms use a variety of metrics that affect calculation of optimal routes

## Slide 47: Routing Algorithms
Routing algorithms often have the following design goals:
Optimality
Simplicity and low overhead
Robustness and stability
Rapid convergence
Flexibility

## Slide 48: Routing Algorithms
Optimality refers to the capability of the routing algorithm to select the best route which depends on the metrics and metric weighting used to make the calculation. Simplicity is where the routing algorithm must offer its functionality within a minimum of software and utilization overhead. Robustness is when the algorithm must perform correctly in the face of unusual or unforeseen circumstances e.g. hardware failures, high load conditions and incorrect implementation.

## Slide 49: Routing Algorithms
Rapid convergence refers to the process of agreement by all routers on optimal routes. Those that converge slowly can cause routing loops. Flexibility refers to algorithms that can quickly and accurately adapt to a variety of network circumstances. The algorithm can be programmed to adapt to changes in network bandwidth and network delays among other variables.

## Slide 50: Routing Algorithms
Algorithm Types
Static versus dynamic: static routing algorithms are hardly algorithms, but are table mappings established by the network administrator before the beginning of the routing. These mappings do not change unless the network administrator changes them. Algorithms that use static routes are simple to design and work well in environments where traffic is relatively predictable and where network design is relatively simple. They don’t react to network changes

## Slide 51: Routing Algorithms
Dynamic routing algorithms adjust to changing network circumstances by analysing incoming routing update messages. If the message indicates that a network change has occurred, the routing software recalculates routes and sends out new routing update messages. These messages permeate the network, stimulating routers to rerun their algorithms and change their routing tables accordingly.

## Slide 52: Routing Algorithms
Single-Path versus multipath: some sophisticated routing protocols support multiple paths to the same destination. Unlike single path algorithms, these multipath algorithms permit traffic multiplexing over multiple lines. They provide better throughput and reliability.

## Slide 53: Routing Algorithms
Flat versus hierarchical: some routing algorithms operate in a flat space, while others use routing hierarchies. In a flat routing system, routers are peers of all others. In a hierarchical routing system, some routers form a routing backbone. Packets from non-backbone routers travel to the backbone routers where they are sent through the backbone until they reach the general area of the destination

## Slide 54: Routing Algorithms
At this point they travel from the last backbone router through one or more non-backbone routers to the final destination. In hierarchical systems some routers in a domain can communicate with routers in other domains while others can communicate only with routers within their domain. The primary advantage of hierarchical routing mimics the organization of most companies and therefore supports their traffic patterns as well.

## Slide 55: Routing Algorithms
Host intelligent versus Router intelligent: some routing algorithms assume that the source end node will determine the entire route. This is usually referred to as source routing. In source routing algorithms routers merely act as store-and-forward devices. Other algorithms assume that hosts know nothing about routes. Routers determine the path through the network based on their own calculations. In the first system the hosts have the routing intelligence while in the latter system routers have the routing intelligence.

## Slide 56: Routing Algorithms
Intra-domain versus inter-Domain: some routing algorithms work only within domains others work within and between domains. The nature of these two algorithm types is different. An optimal intra-domain routing algorithm would not necessarily be an optimal inter-domain routing algorithm.

## Slide 57: Routing Algorithms
Link-state versus Distance Vector: link-state algorithms (shortest path first algorithms) flood routing information to all nodes in the network. Each router however sends only the portion of the routing table that describes the state of its own links. In link-state algorithms each router builds a picture of the entire network in its routing table. Distance vector algorithms call for each router to send all or some portion of its routing table but only to its neighbours. Link-state algorithms are less prone to routing loops than distance vector algorithms because they converge more quickly. Link-state requires more CPU power and memory.

## Slide 58: Routing Metrics
Routing tables contain information used by switching software to select the best route. Routing algorithms use different metrics to determine the best route. Sophisticated routing algorithms can base route selection on multiple metrics, combining them in a single (hybrid) metric. The following metrics are used:

## Slide 59: Routing Metrics
Path length: this is the most common routing metric. Some routing protocols allow network administrators to assign arbitrary costs to each network link. Path length is the sum of the costs associated with each link traversed.
Reliability: refers to the dependability (usually described in terms of the bit-error rate) of each network link. The network administrator can assign reliability ratings to network links.

## Slide 60: Routing Metrics
Routing delay: refers to the length of time required to move a packet from source to destination through the network. It is a common and useful metric. It depends on various factors i.e. bandwidth, port queues at each route along the way, network congestion, physical distance.

## Slide 61: Routing Metrics
Bandwidth: this refers to the available traffic capacity of a link. A 10Mbps Ethernet link would be preferable to a 64Kbps all things being equal. Greater bandwidth does not necessarily provide better routes than routes through slower links. If a faster link is busier, the actual time required to send a packet to the destination could be greater.

## Slide 62: Routing Metrics
Load: the degree to which a network resource such as a router is busy e.g. packets processed per second
Communication cost: some companies may not care about performance as much as they care about operating expenditures.

## Slide 63: Local and Remote Routers
Local routers join network within the same building. Local routers continuously monitor their constituent networks so that routing tables can be updated to reflect network changes. They monitor changes in line speeds, network load, network addressing and network topologies.

## Slide 64: Local and Remote Routers
In the process of joining networks, local routers are used to segment network traffic and to enforce security.
A local router can be used to limit certain type of packets from leaving a specific network segment. It can be used to control which network nodes are able to reach a segment containing sensitive business information.
When a router is employed for security it becomes a firewall on the network, protecting the network from hackers and unwanted traffic.

## Slide 65: Local and Remote Routers
A remote router enables networks to be connected over long distances. For example they connect ATMs, frame relay, high speed serial x.25 networks. They support multiple protocols hence allowing communication with many kinds of distant networks

## Slide 66: Bridges
A bridge is a network device that connects one LAN segment to another. They are used in the following circumstances:
They are used to extend a LAN when the maximum connection limit has been reached such as 30-node limit for an Ethernet segment
They are used to extend a LAN beyond the length limit e.g. 500m for Ethernet
Used to segment LAN to reduce traffic bottlenecks
They are used for security purposes to prevent unauthorised access.

## Slide 67: Bridges
A bridge intercepts all traffic network and examines each packet as it’s received.
It reads the destination address on each packet and determines if the packet should be forwarded to the next network.
If the packet is intended for a local node, the bridge will filter the packet to that node on the originating LAN

## Slide 68: Bridges
A standard Ethernet bridge can filter about 30,000 packets per second and forward about 15,000 packets per second.
Bridges can be programmed to reject all frames sourced from a particular network.
The bridge will act as a firewall for some potentially damaging network packets. They operate at the data link layer on the OSI layer.

## Slide 69: Bridges
Bridges can be grouped in different characteristics based on various product characteristics.
One of these categories classifies bridges as either local or remote.
Local bridges provide a direct connection between multiple LAN segments in the same area.
It is also used to segment network traffic for the purpose of reducing bottlenecks. E.g. a network may have a file server that creates high volume network traffic , a bridge can be installed so packets from that file server only reach workstations in a designated area

## Slide 70: Bridges
Remote bridges on the other hand connect multiple LAN segments in different areas usually over telecommunication lines and combine them into a single large network.
Remote bridges cannot replace WANs in terms of speed, but they can compensate for speed discrepancies through sufficient buffering capabilities.
If a LAN device capable of 3Mbps transmission rate wants to communicate with a device on a remote LAN, the local bridge must regulate the 3 Mbps data stream so that it does not overwhelm the 64Kbps serial link.

## Slide 71: Bridges
This is done by storing the incoming data in onboard buffers and sending it over the serial link at a rate that the serial link can accommodate.
A bridge performs three important functions: learning, filtering and forwarding.
When it powers on a bridge learns the network topology and addresses on all attached networks. The bridge learns what is on the network by examining the source and destination addresses in the packets it receives

## Slide 72: Bridges
By this means each bridge builds a bridging table so it knows the address of every network node. An Ethernet bridge can store up to 8,192 entries in its table. The bridge then uses its table as the basis for forwarding traffic.

## Slide 73: Bridges
When a packet is received the bridge reads the destination address and looks up the address in the bridging table.
If an association is found, the bridge forwards the packet to a known destination. If no association exist, the frame can be flooded to all ports on the bridge except the port from which the frame was sent.
A bridge may also contain instructions entered by the network administrator not to flood packets from specified sources or to discard certain packets instead of forwarding them.

## Slide 74: Bridges
Some bridges can only link 2 network segments. E.g bridge A connects LAN 1 and LAN 2, bridge B connect LAN2 and LAN 3. A packet from LAN1 will have to go through both bridge A and B to reach LAN 3.
Multiport bridges tie several segments into one. There are up to 52 port bridges. A packet from any one of the LANs would travel through only one bridge to reach its destination.

## Slide 75: Bridges
Bridges are installed in parallel on many networks so that if one fails the other will continue.
However sometimes they can create a situation where packets are duplicated by each bridge creating a looping condition where the receiving LAN forwards the packets back.
The loop will continue until one of the bridges stops forwarding.

## Slide 76: Bridges
Spanning Tree Algorithm:
Networks that employ more than one bridge use the spanning tree algorithm. It’s designed to accomplish two goals:
Ensure that a packet cannot be caught in an endless loop on the network
Forward packets along the most efficient route in terms of distance and utilization of cable resources.

## Slide 77: Bridges
Each bridge is given an ID and priority. A root bridge is selected and given high priority.
The spanning tree algorithm protocol enables bridges to “talk” to one another using reserved multicast packets called Bridge Protocol Data Units (BPDUs) which allows bridges to learn about each other.

## Slide 78: Bridges
The first stage in the creation of a bridged network is to determine which bridge has the highest priority. The bridge with the lowest MAC address is assigned the highest priority and becomes the root bridge. The other bridges are given a priority number based on their MAC address. Bridges with lower MAC addresses have higher priority assignments. Once a root bridge is designated, it sends out root BPDUs to find loops.

## Slide 79: Bridges
The other bridges place selected ports in a blocked state to prevent looping. Ports are blocked based on a determination of cost. Each port is assigned a cost value. The cost of a path to the root bridge is based on line speed and distance. Once the spanning tree network is established, the root bridge transmits hello BPDUs once every few seconds. If the other network bridges do not receive hello BPDU within a given time it is assumed that the root bridge is off-line or malfunctioning.

## Slide 80: Bridges
The bridge that detects this first issues a topology change configuration BPDU to establish another root bridge. The spanning tree algorithm allows only one path to any network in a bridged network. By coupling this with cost determination, network congestion is minimized and network efficiency is maximised.

## Slide 81: SWITCHES
Switches are similar to bridges but usually have more ports and unlike bridges which use software to create and manage filter tables, switches use application-specific integrated circuits (ASICs) to build and maintain their filter tables. Switches enable multiple physical LAN segments to be interconnected into a single larger network. Switches forward and flood traffic based on MAC addresses.

## Slide 82: SWITCHES
It can use different forwarding techniques including:
Store-and-Forward switching: an entire frame must be received before its forwarded. The larger the frame sizes the longer the delay through the switch.
Cut-through switching: allows the switch to begin forwarding the frame when enough of the frame is received to make a forwarding decision.
Store-and-forward switching gives the switch the opportunity to evaluate the frame for errors before forwarding it. This capacity to not forward frames containing errors is one of the advantages of switches.

## Slide 83: SWITCHES
If the switch does not know where to send the frame, it broadcasts the frame out to all its ports to the network to learn the correct destination. When the frames reply is returned, the switch learns the location of the new address and adds the information to the switching table. Since the switch now has both of the relevant MAC addresses in its filtering table the two devices can now make a point-to-point connection.

## Slide 84: SWITCHES

## Slide 85: SWITCHES
When the switch is powered on it has nothing in its MAC address forward/filter table. But when the hosts start communicating, the switch places the source hardware address of each frame in the table along with the port that the frame’s address corresponds to. For example in figure 1 above, host A sends a frame to host B. Host A’s MAC address is 0000.8c01.000A; Host B’s MAC address is 0000.8c01.000B. The switch receives the frame from host A on the E0/0 interface and places the source address in the MAC address table

## Slide 86: SWITCHES
Since the destination address is not in the MAC database, the frame is forwarded out to all interfaces except the source port. Host B receives the frame and responds to host A. the switch receives this frame on interface E0/1 and places the source hardware address in the MAC database. Host A and B can now make a point-to-point connection and only the two devices will receive the frames. Hosts C and D will not see the frames nor are their MAC addresses found in the database because they have not yet sent a frame to the switch

## Slide 87: SWITCHES
If Host A and Host B do not communicate to the switch again within a certain amount of time, the switch will flush their entries from the database to keep it as current as possible. MAC Forward/Filter Table:
E0/0: 0000.8c01.000A Step2
E0/0: 0000.8c01.000B Step 4
E0/2:
E0/3:

## Slide 88: SWITCHES
Forward/Filter Decisions:
When a frame arrives at a switch interface, the destination hardware address is compared to the forward/filter MAC database. If the destination hardware address is known and listed in the database, the frame is only sent out to the correct exit interface. The switch does not transmit the frame out any interface except for the destination interface. This preserves bandwidth on the other network segments and is called frame filtering.
If a host or server sends a broadcast on the LAN, the switch will flood the frame out all active ports except the source port by default.

## Slide 89: SWITCHES
Port Security:
It is important to stop just anyone from plugging a host into one of your switch ports or adding a hub, switch or access point into the Ethernet jack. Remember by default MAC addresses will just dynamically appear in your MAC forward/filter database. You can stop this by using port security as in the example below:

## Slide 90: SWITCHES
Switch#Config t
Switch(Config)#int f0/1
Switch(Config-if)#switch port-security?
Aging Port-Security aging commands
Mac-address secure MAC address
Maximum max secure addresses
Violation security violation mode
<cr>

## Slide 91: SWITCHES
You can assign individual MAC addresses to each switch port, you can set up a switch port to allow only one host per port and to shut down the port if the rule is violated.
Switches are layer 2 devices. Layer 2 addresses are determined by the manufacturer of the data communication equipment used. It assumes a flat address space with universally unique address.
Switches also use the Spanning Tree Protocol (STP) to stop network loops. When a switch is first powered on the MAC forward/filter table is empty.

## Slide 92: SWITCHES
The frames in a switched network do not have time to live (TTL) like IP packets traversing routers. As a result if they are not terminated they continue to bounce from switch to switch. Therefore the STP is employed.
Loops result in high CPU load on all switches caught in the loop, because the same frames are constantly being forwarded back and forth. This slows down performance on the switch when legitimate traffic arrives.

## Slide 93: SWITCHES
A host caught in a network loop is not accessible to other hosts on the network because the MAC address table is constantly changing with the updates from the broadcast frames, the switch does not know which port to forward the unicast frames out to reach the final destination.

## Slide 94: SWITCHES
A broadcast storm occurs when there are so many frames caught in a layer 2 loop that all available bandwidth is consumed. The storm can also cause the end device to malfunction because of high processing requirements for sustaining such a high traffic load on the network interface card.

## Slide 95: SWITCHES
STP ensures that there is only one logical path between all destinations on the network by intentionally blocking redundant paths that could cause a loop.
A port is considered blocked when network traffic is prevented from entering or leaving that port. This does not include the bridge protocol data unit (BPDU).

## Slide 96: Communication servers
Communication servers provide a way to connect terminals, PCs, modems and printers into a network. A single communication server has multiple serial ports available for use and a port that is connected to the network. A typical use for a communication server is to connect terminals to a network so they can reach a host system.

## Slide 97: Multiplexers
Multiplexing is a process in which multiple data channels are combined into a single data or physical channel at the source. Multiplexing can be implemented at any OSI layer. Demultiplexing is the process of separating multiplexed data channels at the destination e.g. when data from multiple devices is combined into a single physical channel using a multiplexer, or when data from multiple applications is multiplexed into a single lower layer data packet.

## Slide 98: Multiplexers
A multiplexer is a physical layer device that combines multiple data streams into one or more output channels at the source. Multiplexers demultiplex the channels into multiple data streams at the remote end and this maximizes the use of the bandwidth of the physical medium by enabling it to be shared by multiple traffic source.

## Slide 99: Multiplexers
Multiplexing is accomplished by one of any of the three methods below:
Time Division Multiple Access (TDMA) or TDM: this divides the channels into distinct time slots. Each time slot is designated for a particular network node as if it were a dedicated line. The multiplexer rotates from time slot to time slot for each channel. It does not guarantee the most efficient use of the network medium since transmission occurs on only one channel at a time. A node may transmit at an interval that is out of synchronoization with its time slot.

## Slide 100: Multiplexers
Asynchronous Time Division multiplexing (ATDM): Information from data channels is allocated bandwidth as needed by using dynamically assigned time slots
Frequency Division Multiplexing (FDM) or Frequency Division Multiple Access (FDMA): Information from each data channel is allocated bandwidth based on the signal frequency of the traffic, each channel has its own broadcast frequency. The multiplexer switches from frequency to frequency as it sends data.

## Slide 101: Multiplexers
Statistical Multiplexing: The physical medium bandwidth is dynamically allocated based on the application need. The multiplexer continually monitors each channel to determine the communication requirements.

## Slide 102: Repeaters
Once a network is installed, more and more departments are likely to request connectivity to the network. Network growth can be significant in terms of new users and the distances between the users. Extending cable plant runs throughout a floor or building presents a challenge. Several users may be spread over distances that require cabling to extend beyond the IEEE distance specifications.

## Slide 103: Repeaters
A repeater is a solution that enables a network to reach users in distant portions of a building. It amplifies an incoming signal, retimes it and reproduces it along multiple cable runs. Retiming helps to avoid packet collision once the signal is placed on the cable. According to IEEE specifications and depending on the topology and media a single packet can travel through up to four repeaters. If the repeater detects a problem on an individual segment, such as excessive collisions it halts transmission of data to that segment. This method of closing down a segment is called partitioning.

## Slide 104: OPEN SYSTEMS INTERCONNECTION(OSI) REFERENCE MODEL
OSI reference model describes how information from a software application in one computer moves through a network medium to a software application in another computer. It is composed of seven layers, each specifying particular network functions. It was developed by the International Organisation for Standards (ISO) in 1984. The OSI model divides the tasks involved with moving information between networked computers into seven smaller more manageable task groups.

## Slide 105: OPEN SYSTEMS INTERCONNECTION(OSI) REFERENCE MODEL
A task or group of tasks is then assigned to each of the seven OSI layers. Each layer is independent so that the tasks assigned to each layer can be implemented independently. This enables the solutions offered by one layer to be updated without adversely affecting the other layers.

## Slide 106: OPEN SYSTEMS INTERCONNECTION(OSI) REFERENCE MODEL

## Slide 107: OPEN SYSTEMS INTERCONNECTION(OSI) REFERENCE MODEL
The seven layers of the OSI reference model can be divided into two categories, upper layers and lower layers. The upper layers of the OSI model deal with application issues and generally are implemented only in software. The lower layers of the OSI model handle data transport issues

## Slide 108: OPEN SYSTEMS INTERCONNECTION(OSI) REFERENCE MODEL
The OSI model provides a conceptual framework for communication between computers but the model itself is not a method of communication. Actual transmission is made possible by using communication protocols. A protocol is a formal set of rules and conventions that governs how computers exchange information over a network medium. A protocol implements the functions of one or more of the OSI layers. Some of the protocols include LAN protocols, WAN protocols, Network protocols and Routing protocols.

## Slide 109: OPEN SYSTEMS INTERCONNECTION(OSI) REFERENCE MODEL
LAN protocols operate at the physical and data link layers of the OSI model and define communication over the various LAN media. WAN protocols operate at the lowest three layers and define communication over WAN media. Routing protocols are network layer protocols that are responsible for exchanging information between routers so that the routers can select the proper path for network traffic.

## Slide 110: OPEN SYSTEMS INTERCONNECTION(OSI) REFERENCE MODEL
OSI Model and Communication Between Systems:
Information being transferred from a software application in one computer system to a software application in another must pass through the OSI layers. For example if a software application in system A has information to transmit to a software application in system B, the application program in system A will pass its information to the application layer of system A.

## Slide 111: OPEN SYSTEMS INTERCONNECTION(OSI) REFERENCE MODEL
The application layer passes information to the presentation layer, which relays the data to session layer and so on down to the physical layer. At the physical layer the information is placed on the physical network medium and is sent across the medium to system B.

## Slide 112: OPEN SYSTEMS INTERCONNECTION(OSI) REFERENCE MODEL
The physical layer of system B removes the information from the physical medium and then its physical layer passes the information up to the data link layer which passes it to the network layer and so on until it reaches the application layer of system B. finally the application layer of system B passes the information to the recipient application software to complete the communication process.

## Slide 113: OPEN SYSTEMS INTERCONNECTION(OSI) REFERENCE MODEL
Interaction between OSI Model Layers:
A given layer in the OSI model generally communicates with three other OSI layers. The layer directly above it, the layer directly below it and its peer layer in other networked computer system. The datalink in system A for example communicates with the network layer of system A, the physical layer of system A, and the data link layer in system B.

## Slide 114: OPEN SYSTEMS INTERCONNECTION(OSI) REFERENCE MODEL
OSI Layer Services:
Three basic elements are involved in layer services;
(1) The service user: this is the OSI layer that request services from an adjacent OSI layer.
(2) The service access point: this is a conceptual location at which one OSI layer can request the services of another OSI layer.
(3) The service provider: this is the OSI layer that provides services to service users OSI layers can provide services to multiple service users.

## Slide 115: OPEN SYSTEMS INTERCONNECTION(OSI) REFERENCE MODEL
OSI model and Information Exchange:
The seven layers use various forms of control information to communicate with their peer layers in other computer systems. This control information consists of specific requests and instructions that are exchanged between peer OSI layers. Control information takes two forms i.e. headers and trailers.

## Slide 116: OPEN SYSTEMS INTERCONNECTION(OSI) REFERENCE MODEL
Information exchange process occurs between peer OSI layers. Each layer in the source system adds control information to data and each layer in the destination system analyses and removes the control information from that data. If system A has data to send to system B, the data is passed to the application layer in A. the application layer in A, communicates any control information required by the application layer in B by pre-appending a header to the data.

## Slide 117: OPEN SYSTEMS INTERCONNECTION(OSI) REFERENCE MODEL
The resulting information unit ( a header and data) is passed to the presentation layer, which pre-appends its own header containing control information intended for the presentation layer in B. the information unit grows in size as each layer pre-appends its own header ( in some cases a trailer) that contains control information to be used by its peer.
The physical layer in system B receives the information unit and passes it to the data link layer. The data link layer in B then reads the control information contained in the header pre-appended by the datalink in A. the header is then removed and the information unit is allowed to proceed to the network layer. Each layer performs the same action.

## Slide 118: The Physical Layer
The physical layer defines the electrical, procedural and functional specifications for activating, maintaining and deactivating the physical link between communicating network systems. Physical layer specifications define characteristics such as voltage levels, timing of voltage changes, physical data rates, maximum transmission distances and physical connectors. Physical layer implementation can be categorised as either LAN or WAN specifications.

## Slide 119: The Physical Layer

## Slide 120: DATA LINK LAYER
The data link layer provides reliable transit of data across a physical network link. Different data link layer specifications define different network and protocol characteristics including physical addressing, network topology, error notification, sequencing of frames and flow control. Physical addressing defines how devices are addressed at the data link layer. Network topology consists of data link layer specifications that often define how devices are to be physically connected such as in a bus or ring topology.

## Slide 121: DATA LINK LAYER
Error notification alerts upper layer protocols that a transmission error has occurred and the sequencing of data frames re-orders frames that are transmitted out of sequence. Flow control moderates the transmission of data so that the receiving device is not overwhelmed with more traffic than it can handle at any one time.

## Slide 122: DATA LINK LAYER
The Instititute of Electrical and Electronics engineers (IEEE) subdivides the data link layer into two sub layers; Logical Link Control (LLC) and Media Access Control (MAC).

## Slide 123: DATA LINK LAYER
The LLC sublayer of the data link layer manages communication between devices over a single link of a network. It is defined in IEEE 802.2 specifications and supports both connectionless and connection oriented services used by higher level protocols. Its responsible for any flow control and error connection. LLC handles both connectionless and connection oriented services. In connection-oriented service not all network devices run at the same speed. The LLC supports flow control in the following ways:

## Slide 124: DATA LINK LAYER
(a) Sliding window: allows the two communicating devices to negotiate the number of allowable outstanding frames. The receiving device does not need to acknowledge each frame it receives, it can send one acknowledgement for a group of frames
(b) Stop and wait: a green light way of handling flow control. When the receiving device has no memory left to store incoming data, it suspends transmission. When memory is free again, it sends a signal to the transmitting device to resume.

## Slide 125: DATA LINK LAYER
Error control is implemented using Cyclic Redundancy Checks (CRCs) and check sums. A CRC is a method of detecting errors in the transmission of data. Before data is send a CRC number is calculated by running the data through an algorithm and producing a unique number. At the receiving end of transmission, the data is run through the same algorithm again to produce the number. If the numbers match the data is error free. The unique value generated from the algorithm is called a checksum.

## Slide 126: DATA LINK LAYER
The MAC sub-layer of the data link layer manages protocol access to the physical network medium. The IEEE MAC specification defines MAC addresses, which enable multiple devices to uniquely identify one another at the data link layer.
Data link addresses usually exist within a flat address space and have a pre-established and typically fixed relationship to a specific device. End systems generally have only one physical network connection and thus have only one data link address. Routers and other inter-networking devices have multiple physical network connections and therefore have multiple data-link addresses.

## Slide 127: DATA LINK LAYER
MAC addresses are 48 bit in length and are expressed as 12 hexadecimal digits. The first 6 digits which are administered by IEEE, identify the manufacturer or vendor and therefore comprises the Organisationally Unique Identifier (OUI). The last 6 digits comprise the interface serial number, or another value administered by the specific vendor. MAC addresses are sometimes called the Burned-in-Addresses (BIAS) because they are burned into ROM and are copied in the RAM when the interface card initializes.

## Slide 128: DATA LINK LAYER
Three ways used to control access to media are:
(a) Addressing : the data link layer is responsible for the physical addresses of devices on the network. Every device on the network has a hard coded address attached to it, MAC address.

## Slide 129: DATA LINK LAYER
(b) Contention: in a contention based network any device can transmit whenever it needs to. This allows equal access to the network media but so may collisions. On contention based networks devices listen for other signals on the media before transmitting. This is known as Carrier Sense Multiple Access (CSMA). The two types under this are CSMA/CD and CSMA/CA. CSMA/CD stands for CSMA/Collision Detection.

## Slide 130: DATA LINK LAYER
The transmission sequence for CSMA/CD is as follows: the device listens to the media for any transmission, if the network media is quiet then the device proceeds to start transmitting its data.
After the device transmits its data it listens to the network media to detect any collisions. If the device detects a collision ,it sends out a signal to all devices. This signal tells the other devices to keep from sending data for a small period to clear all signals from the media.
The transmitting stations will then wait a random amount of time before sending their data. If a second collision occurs the above steps are repeated, but they double the random time-out before they transmit again. Ethernet uses the CSMA/CD

## Slide 131: DATA LINK LAYER
CSMA/Collision Avoidance on the other hand works differently. The device wanting to send checks the media for any active transmissions. If the media is clear the device sends a request to send a message. If its okay to transmit the networker server responds with a clear to send signal. When the device receives the clear to send signal it transmits its data. After the transmission is completed the device sends out an abort signal that it has finished.

## Slide 132: DATA LINK LAYER
(3).Deterministic: unlike a contention-based network a deterministic network has a system that determines transmitting order. The two types of deterministic networks are token passing and polling.

## Slide 133: NETWORK LAYER
The network layer defines the network address, which differs from the MAC address. Some network layer implementations, such as the Internet Protocol (IP) define network addresses in a way that route selection can be determined systematically by comparing the source network address with the destination network address and applying the sub net mask.
Because this layer defines the logical network layout, routers use this layer to determine how to forward packets. Because of this, much of the design and configuration work for networks happens at layer 3, the network layer.

## Slide 134: TRANSPORT LAYER
The transport layer accepts data from the session layer and segments the data for transport across the network. The layer is responsible for making sure that the data is delivered error-free and in the proper sequence. Flow control generally occurs at the transport layer. Flow control manages data transmission between devices so that the transmitting device does not send more data than the receiving device can process.

## Slide 135: TRANSPORT LAYER
Multiplexing enables data from several applications to be transmitted into a single physical link. Virtual circuits are established, maintained and terminated by the transport layer. Error checking involves creating various mechanisms for detecting transmission errors, while error recovery involves acting such as requesting that data be retransmitted to resolve any errors that occur.

## Slide 136: SESSION LAYER
The session layer establishes, manages and terminates communication sessions. Communication sessions consist of service requests and service responses that occur between applications located in different network devices.
These requests and responses are co-ordinated by protocols implemented at the session layer. Some examples of session layer implementation include Zone Information Protocol (ZIP), Appletalk protocol, Session Control Protocol (SCP).

## Slide 137: PRESENTATION LAYER
The presentation layer provides a variety of coding and conversion functions that are applied to application layer data. These functions ensure that information sent from the application layer of one system would be readable by the application layer of another system. Some examples of presentation layer coding and conversion schemes include common data representation formats, conversion of character representation formats, common data compression schemes, and common data encryption schemes.

## Slide 138: PRESENTATION LAYER
Common data representation formats, or the use of standard image, sound and video formats enable the interchange of application data between different types of computer systems.
Conversion schemes are used to exchange information with systems by using different text and data representations e.g. American Standard Code for Information Interchange (ASCII), which uses 8 bits to represent up to 256 different characters and Extended Binary Coded Decimal Interchange Code (EBCDIC) which uses 7 bits to allow up to 128 characters.

## Slide 139: PRESENTATION LAYER
Standard data compression schemes enable data that is compresses at the source device to be properly decompressed at the destination.
Standard data encryption enables data encrypted at the source to be properly deciphered at the destination.

## Slide 140: PRESENTATION LAYER
Presentation layer implementations are not typically associated with a particular protocol stack. Some well known standards for video include Quick Time and Motion Picture Experts Group (MPEG). Quick Time is an Apple computer specification for video and audio and MPEG is a standard for video compression and coding.

## Slide 141: PRESENTATION LAYER
Among the well known graphic image formats are Graphics Interchange Formats (GIF), Joint Photographic Experts Group (JPEG) and Tagged Image File Format ( TIFF). GIF is a standard for compressing and coding graphic images. JPEG is another compression and coding standard for graphic images and TIFF is a standard coding format for graphic images.

## Slide 142: APPLICATION LAYER
The application layer is the closest to the end user, which means that both the application layer and the user interact directly with the software application. This layer interacts with the software applications that implement a communicating component.
Such applications fall outside the scope of the OSI model. Application layer functions typically include identifying communication partners, determining resource availability and synchronizing communication. Some examples of application layer implementations include Telnet, File Transfer Protocol (FTP) and Simple Mail Transfer Protocol ( SMTP).

## Slide 143: INFORMATION FORMATS
The data and control information that is transmitted through networks takes a variety of forms. The terms used for these formats are not used consistently but sometimes interchangeably. Common information formats include; frames, packets, datagrams, segments, messages, cells and data units.

## Slide 144: INFORMATION FORMATS
A frame is an information unit whose source and destination are data link layer entities. A frame is composed of the data link layer header and trailer and upper layer data. The header and trailer contain control information intended for the data link layer entity in the destination system.

## Slide 145: INFORMATION FORMATS

## Slide 146: INFORMATION FORMATS
A packet is an information unit whose source and destination are network layer entities. A packet is composed of the network layer header and possibly a trailer and upper layer data. The header and the trailer contain control information intended for the network layer entity in the destination system.

## Slide 147: INFORMATION FORMATS

## Slide 148: INFORMATION FORMATS
The term data gram usually refers to an information unit whose source and destination are network layer entities that use connectionless network service.
The term segment refers to an information unit whose source and destination are transport layer entities.
A message is an information unit whose source and destination entities exist above the network layer often at the application layer.

## Slide 149: INFORMATION FORMATS
A cell is an information unit of a fixed size whose source and destination are data link layer entities. Cells are used in switched environments such as Asynchronous Transfer Mode (ATM) and Switched Multimegabit Data Scheme (SMDS) networks.
A cell is composed of a header and a payload. The header contains control information intended for the destination data link layer and it is 5 bytes long. The payload contains upper layer data that is encapsulated in the cell header and is typically 48 bytes long

## Slide 150: INFORMATION FORMATS

## Slide 151: INFORMATION FORMATS
Data unit is a generic term that refers to a variety of information units e.g. Service Data Units (SDUs) , protocol data units, Bridge Protocol Data Units (BPDUs).

## Slide 152: ISO HIERARCHY OF NETWORKS
Large networks are organised as hierarchies by the International Organisation for Standardisation (ISO). The key one are:
(a) End System (ES): this is a network device that does not perform routing or other traffic forwarding functions e.g. terminals, PCs and printers

## Slide 153: ISO HIERARCHY OF NETWORKS
(b) Intermediate System (IS): device that performs routing or other traffic forwarding functions e.g. routers, switches and bridges. Two types of IS exist namely intra domain and inter domain. Intra domain communicates within a single autonomous system whereas an inter domain IS communicates within and between autonomous systems.

## Slide 154: ISO HIERARCHY OF NETWORKS
(c) Autonomous System (AS): a collection of networks under a common administration that share a common routing strategy. Autonomous systems are subdivided into areas and an AS is sometimes called a domain.

## Slide 155: Connection-Oriented and Connectionless
Transport protocols can be characterised as being either connection oriented or connectionless. Connection oriented services must establish a connection with the desired service before passing any data. The services involves connection establishment, data transfer and connection termination. The communicating services may negotiate and establish certain criteria for the transfer. When data is being transferred most connection oriented services will monitor for lost packets and handle resending.
Connectionless transfer send the data without the added overhead of creating and terminating a connection. Both have their place in networks.

## Slide 156: TRANSMISSION CONTROL PROTOCOL/INTERNET PROTOCOL (TCP/IP)
The TCP/IP suite was created by the Department of Defence to ensure and preserve data integrity as well as maintain communication in the event of catastrophic war.
The diagram below shows a the TCP/IP protocol suite.

## Slide 157: TRANSMISSION CONTROL PROTOCOL/INTERNET PROTOCOL (TCP/IP)

## Slide 158: TRANSMISSION CONTROL PROTOCOL/INTERNET PROTOCOL (TCP/IP)
Note that the DOD model is similar in concept with the OSI reference model. Where the process/application correspond to the Application, Presentation and session layers of the OSI
Host-to-Host corresponds to the Transport layer. The Internet layer corresponds to the Network layer and the Network access corresponds to the Data link and physical Layer

## Slide 159: TRANSMISSION CONTROL PROTOCOL/INTERNET PROTOCOL (TCP/IP)
The internet protocols are the world’s most popular open systems protocol suite because they can be used to communicate across any set of interconnected networks and are equally suited for LAN and WAN communications.
The internet protocols consist of a suite of communication protocols of which the two best known are the Transmission control Protocol (TCP) and the Internet Protocol (IP).

## Slide 160: TRANSMISSION CONTROL PROTOCOL
The TCP protocol works at the host-to-host layer protocols. The TCP takes large blocks of information from an application and breaks them into segments. It numbers and sequences each segment so that the destinations’ TCP stack can put the segments back into the order the application intended.

## Slide 161: TRANSMISSION CONTROL PROTOCOL
Before a transmitting host starts to send segments down the model, the senders TCP stack contacts the destination’s TCP stack to establish a connection. What is created is known as a virtual circuit. During this initial handshake the two TCP layers also agree on the amount of information that is going to be sent before the recipient’s TCP sends back an acknowledgement.

## Slide 162: TCP SEGMENT FORMAT

## Slide 163: TCP SEGMENT FORMAT
The TCP header is 20 bytes long or up to 24 bytes with options.
Source Port: The port number of the application on the host sending the data.
Destination Port: The port number of the application requested on the destination host.
Sequence Number: A number used by TCP that puts the data back in the correct order or retransmits missing or damaged data, a process called sequencing.

## Slide 164: TCP SEGMENT FORMAT
Acknowledgement Number: The TCP octet that is expected next.
Header Length: The number of 32-bit words in the TCP header. This indicates where the data begins. The TCP header is an integral number of 32 bits in length.
Reserved: Always set to zero
Code Bits: Control functions used to set up and terminate a session.

## Slide 165: TCP SEGMENT FORMAT
Window: The window size the sender is willing to accept in octets.
Checksum: The cyclic redundancy check checks the header and the data fields.
Urgent: A valid field only if the Urgent pointer in the code bits is set. If so, this value indicates the offset from the current sequence number, in octets, where the first segment of non-urgent data begins.

## Slide 166: TCP SEGMENT FORMAT
Options: May be 0 or a multiple of 32 bits if any. What this means is that no options have to be present (option size of 0). However if any options are used that do not cause the option field to total a multiple of 32 bits, padding of 0s must be used to make sure the data begins on a 32-bit boundary.
Data: Handed down to the TCP protocol at the transport layer, which includes the upper layer headers.

## Slide 167: INTERNET PROTOCOL (/IP)
The IP is a network layer protocol that contains addressing information and some control information that enables packets to be routed. Along with TCP, IP represents the heart of the internet protocols. IP has two primary responsibilities

## Slide 168: INTERNET PROTOCOL (IP)
(1) Providing connectionless best effort delivery of datagrams through an internetwork.
(2) Providing fragmentation and reassembly of datagrams to support data links with different maximum transmission unit (MTU) sizes.

## Slide 169: INTERNET PROTOCOL (IP)

## Slide 170: INTERNET PROTOCOL (IP)
Version: Indicates the version of IP currently used
IP Header Length (IHL): Indicates the datagram header length in 32 bit word
Type of Service: Specifies how an upper layer protocol would like a current datagram to be handled and assigns datagrams various levels of importance
Total Length: Specifies the length, in bytes, of the entire IP packet including the data and the header

## Slide 171: INTERNET PROTOCOL (IP)
Identification: contains an integer that identifies the current datagram. This field is used to help put together datagram fragments.
Flags: consist of 3-bit field of which the two low order bits control fragmentation. The low order bit specifies whether the packet can be fragmented. The middle bit specifies whether the packet is the last fragment in a series of fragmented packets.

## Slide 172: INTERNET PROTOCOL (IP)
Fragment Offset: indicates the position of the fragments data relative to the beginning of the data in the original datagram, which allows the destination IP process to properly reconstruct the original datagram
Time-to-Live: maintains a counter that gradually decrements down to zero, at which point the datagram is discarded. This keeps packets from looping endlessly

## Slide 173: INTERNET PROTOCOL (IP)
Protocol: indicates which upper layer protocol receives incoming packets after IP processing is completed.
Header Checksum: helps ensure IP header integrity
Source Address: specifies the sending node
Destination Address: specifies the receiving node
Options: Allows IP to support various options such as security
Data: contains upper-layer information.

## Slide 174: IP ADDRESSING
An IP address is a numeric identifier assigned to each machine on an IP network. It designates the specific location of a device on the network. IP address is a software address not a hardware address.
IP addressing was designed to allow hosts on one network to communicate with a host on a different network regardless of the type of LANs the hosts are participating in.

## Slide 175: IP ADDRESSING
IP addressing scheme is integral to the process of routing IP datagrams through a network. IP addresses can be sub-divided and used to create addresses for subnetworks.
Each host on a TCP/IP network is assigned a unique 32-bit logical address that is divided into two main parts, the network number and the host number.

## Slide 176: IP ADDRESSING
The network number identifies a network and must be assigned by the internet network information center (InterNic) if the network is part of the internet. An Internet Service Provider ( ISP) can obtain blocks of network addresses from the InterNic and can itself assign address space as necessary.
The host number identifies a host on a network and is assigned by the local network administrator

## Slide 177: IP ADDRESS FORMAT
The 32-bit IP address is grouped 8 bits at a time, separated by dots and represented in decimal format (known as dotted decimal notation). Each bit in the octet has a binary weight (128, 64, 32, 16, 8,4,2,1).
The maximum value for an octet is 255 and the minimum is 0.

## Slide 178: IP ADDRESS FORMAT

## Slide 179: IP ADDRESS FORMAT
Example:
Dotted-decimal; 172.16.30.56
Binary; 10101100.00010000.00011110.00111000
Hexadecimal; AC.10.1E.38
All the three above represent the same IP address.

## Slide 180: IP ADDRESS CLASSES
IP addressing supports five different address classes A,B,C,D and E. Only classes A, B and C are available for commercial use. The left most (high order ) bits indicate the network class.

## Slide 181: IP ADDRESS CLASSES

## Slide 182: IP ADDRESS CLASSES
The class of address can be determined easily by examining the first octet of the address and mapping that value to a class range in the table below:

## Slide 183: IP ADDRESS CLASSES

## Slide 184: IP ADDRESS CLASSES
The High-order bits: The designers of the IP scheme said that the first bit of the first byte in a class A network must always be off, 0. This means that a class A address must be between 0 and 127 in the first byte.
Consider the following network address:
0xxxxxxx

## Slide 185: IP ADDRESS CLASSES
If we turn the other 7 bits all off and then turn them all on we will find the class A range of network addresses to be:
00000000 = 0
01111111 = 127
Though 0 and 127 are not valid in a class A network. They are reserved. 0 reserved for default route and 127 reserved for diagnostics.

## Slide 186: IP ADDRESS CLASSES
In a class B network the first bit of the first byte must always be turned on but the second bit must always be turned off. If you turn the other 6 bits all off and then all on, you will find the range for class B network:
10000000 = 128
10000000 = 191

## Slide 187: IP ADDRESS CLASSES
For class C networks, the first 2 bits of the first octet as always turned on, but the third bit is always off. The range for class C then is:
11000000 = 192
11011111 = 223

## Slide 188: Reserved IP Addresses
Network address of all 0s interpreted to mean “this network or segment”
Network address of all 1s interpreted to mean “all networks”
Network 127.0.0.1 is reserved for loopback tests
Node address of all 0s interpreted to mean “all nodes” on a specified network

## Slide 189: Reserved IP Addresses
Node address of all 1s interpreted to mean “all nodes” on the specified network, for example 128.2.255.255 means all nodes on the network 128.2 (class B)
Entire IP address set to all 0s, used by routers to designate the default route.
Entire IP address set to all 1s ( 255.255.255.255), broadcast to all nodes on the current network.

## Slide 190: Maximum Hosts
Each class A address has 3 bytes (24-bit positions) for the node address. This means there are 2 to power 24 or 16,777,216 unique combinations and therefore precisely that many possible unique node addresses for each class A network.
However because node addresses with the two patterns of all 0s and all 1s are reserved the actual maximum usable number of nodes for class A network is 2 to power 24 minus 2, which gives 16,777, 214.

## Slide 191: Maximum Hosts
Example
All host bits off is the network address: 10.0.0.0
All hosts on is the broadcast address: 10.255.255.255
The valid hosts are the numbers in between the network address and the broadcast address i.e. 10.0.0.1 through 10.255.255.254 (repeat the same for class B and C)

## Slide 192: IP Subnet Addressing
IP Networks can be subdivided into smaller networks called sub networks (subnets). Subnetting provides the network administrator with several benefits including extra flexibility, more efficient use of network addresses and the capability to contain broadcast traffic.

## Slide 193: IP Subnet Addressing
The question you need to ask as a network administrator is what happens if you want to take one network address and create six networks from it.
You would have to do something called sub-netting because that is what allows you to take one larger network and break it into a bunch of smaller networks.

## Slide 194: IP Subnet Addressing
There are various benefits of subnetting which include:
Reduced network traffic
Optimized network performance
Simplified management
Facilitated spanning of large geographical distances, WAN links are considerably slower and more expensive than LAN links, so subnetting will enable connecting multiple smaller networks.

## Slide 195: IP Subnet Addressing
To create subnetworks you take bits from the host portion of the IP address and reserve them to define the subnet address. This means fewer bits for hosts, so the more subnets, the fewer bits available for defining hosts.
For the subnet address scheme to work every machine on the network must know which part of the host address will be used as the subnet address.

## Slide 196: IP Subnet Addressing
This is accomplished by assigning a subnet mask to each machine. A subnet mask is a 32-bit value that allows the recipient of IP packet to distinguish the network portion of the IP address from the host ID portion of the IP address.
The network administrator creates a 32-bit subnet mask composed of 1s and 0s. The 1s in the subnet mask represent the positions that refer to the network or subnet addresses.

## Slide 197: IP Subnet Addressing
Not all networks need subnets, meaning they use the default subnet mask. This is basically the same as saying that a network doesn't have a subnet address.
There are default subnet masks for classes A,B and C.
Class A: 255.0.0.0
Class B: 255.255.0.0
Class C: 255.255.255.0

## Slide 198: IP Subnet Addressing
Subnets are under local administration, as such the outside world sees an organization as a single network and has no detailed knowledge of the organization internal structure. A given network address can be subdivided into many subnets.
For example 172.16.1.0, 172.16.2.0, 172.16.3.0 and 172.16.4.0 are all subnets within network 172.16.0.0 ( all the 0’s in the host portion of an address specifies the entire network